## Slide 1: GenStore: A High-Performance In-Storage Processing System for Genome Sequence Analysis
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun,
Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr,
Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu
P&S SSD: Wednesday, 9 November 2022
Notes: Hi, I’m Nika, and today I will introduce GenStore: A High-Performance In-Storage Processing System
for Genome Sequence Analysis

## Slide 2: Genome Sequence Analysis
Genome sequence analysis is critical for many applications
  Personalized medicine
  Outbreak tracing
  Evolutionary studies
Genome sequencing machines extract smaller fragments of the original DNA sequence, known as reads
AAGCTTCCATGG
AAATGGGCTTTC
GCCCAAATGGTT
GCTTCCAGAATG
Notes: Genome sequence analysis (GSA) is critical for many applications [CLICK]
Genome sequencing machines extract smaller fragments of the original DNA sequence, known as reads. [CLICK]

## Slide 3: Genome Sequence Analysis
Read mapping: first key step in genome sequence analysis
…GCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTCCACAATG…
  Aligns reads to potential matching locations in the reference genome
Reference Genome
Differences
Differences
  For each matching location, the alignment step finds the degree of similarity (alignment score)
AAGCTTCCATGG
GCCCAAATGGTT
GCTTCCAGAATG
AAATGGGCTTTC
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome due to:
  Sequencing errors
  Genetic variation
Notes: Read mapping is the first key step in genome sequence analysis [CLICK]
That Aligns reads to potential matching locations within the reference genome [CLICK]
For each matching location, the alignment step finds the degree of similarity between read and reference by calculating the alignment score
Calculating the alignment score requires computationally-expensive approximate string matching (ASM) to account for differences between reads and the reference genome. [CLICK]

## Slide 4: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement from Storage
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 5: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 6: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 7: Challenges
Read mapping workloads can exhibit different behavior
There are limited hardware resources
in the storage system
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD. By addressing these challenges [CLICK]

## Slide 8: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 9: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: That was a summary of my talk. So let’s start with the background on read mapping so we can dive into the talk in more detail.

## Slide 10: Read Mapping Process
GCC | 7 |  | 
CCC | 8 |  | 
CAA | 1 |  | 
AAA | 31 | 101 | 
CCA | 25 | 230 | 400
… | … | … | …
…CAATTTGCCCATATGGTTAAGCTTCCATGGAAATGGGCTTTCGCTTTG…
Reference
> 3 billion characters
Index
K-mer
Locations
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
Determine potential matching locations (seeds) in the reference genome
Prune some seeds in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
Seeds
…
Notes: Mapping reads to reference genome requires expensive computation on large datasets.
[CLICK] The search space in the Reference genome can be very large (for example the human reference genome contains more than three billion characters).
[CLICK] Therefore, read mappers typically use an index of the reference genome to reduce the search space. This index contains unique 𝑘-length subsequences ([CLICK] called 𝑘-mers) extracted from the reference genome, [CLICK] and locations of these 𝑘-mers in the reference genome.
Read mapping is a three step process. State-of-the-art read mappers involve several heuristics to reduce the cost of expensive alignment computation.
[CLICK] In the first step (seeding), the mapper determines the potential matching locations (seeds) in the large reference genome where the read could map.
[CLICK] To do so, the read mapper extracts k-mers from the read [CLICK] and looks up the k-mer fetched from a read in the reference index. [CLICK] For all the k-mers that hit in the index, the read mapper marks the locations of them in the reference genome as the read’s potential matching locations (or seeds).
To further reduce the cost of the computationally-expensive alignment, the read mapper performs a second step [CLICK] , called chaining or seed filtering, in which the mapper [CLICK] prunes the seeds in the reference to which the read would not align using a simple approximation of the alignment score.
At the end of this step, the reads that have all their locations filtered, skip the third step.
[CLICK] For the remaining reads, the thitd step, which is the costly alignment, determines the exact differences between a read and the reference genome [CLICK] via approximate string matching.

## Slide 11: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: We perform experimental studies to understand the potential of efficient in-storage filters for improving read mapping performance.

## Slide 12: Motivation
Case study on a real-world genomic read dataset
  Various read mapping systems
  Various state-of-the-art SSD configurations
The ideal in-storage filter significantly improves performance by
reducing the computation overhead
reducing the data movement overhead
Notes: We perform a case study on a real world genomic read dataset, on various read mapping systems and state-of-the-art SSD configirations.

## Slide 13: Motivation
Case study on a real-world genomic read dataset
  Various read mapping systems
  Various state-of-the-art SSD configurations
Filtering outside SSD provides lower performance benefit since it
does not reduce the data movement overhead
2) must compete with read mapping for system resources
A HW accelerator reduces the computation bottleneck,
which makes I/O a larger bottleneck in the system
Notes: We perform a case study on a real world genomic read dataset, on various read mapping systems and state-of-the-art SSD configirations.

## Slide 14: Our Goal
Design Objectives:
Design an in-storage filter for genome sequence analysis in a cost-effective manner
Provide high in-storage filtering performance to overlap the filtering with the read mapping of unfiltered data
Performance
Support reads with 1) different properties and 2) different degrees of genetic variation in the compared genomes
Applicability
Do not require significant hardware overhead
Low-cost
Notes: Motivated by these observations, Our goal is to design an in-storage filter for genome sequence analysis in a cost-effective manner. [CLICK]
We have three key objectives in designing our new system. [CLICK]
First, the system should Provide high in-storage filtering performance to overlap the filtering with the read mapping of unfiltered data
Second, the design should Support reads with 1) different properties and 2) different degrees of genetic variation
Third, it should not require significant additional hardware overhead

## Slide 15: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: To this end, we propose GenStore…

## Slide 16: GenStore
SSD Controller
Core
Core
Core
In-SSD DRAM
L2P
Mappings
Flash
Ctrl.#1
Flash
Ctrl.#N
⋯
NAND
Die#4
NAND
Die#1
⋯
NAND
Die#4
NAND
Die#1
⋯
Host System
FTL
ACC
ACC
ACC
GenStore
Metadata
GenStore
FTL
Reads that need
substantial processing
Key idea: Filter reads that do not require alignment inside the storage system
Challenges
  Different behavior across read mapping workloads
  Limited hardware resources in the SSD
Notes: Which is the first in-storage processing system designed for genome sequence analysis
Our key idea is to Filter reads that do not require alignment inside the storage system and send the unfiltered data to the host system for further processing
However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD.

## Slide 17: Filtering Opportunities
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate and short
  Long reads: less accurate and long
High sequencing error rates (long reads) or
High genetic variation (short or long reads)
Non-matching reads
Do not have potential matching locations, so they skip alignment
Low sequencing error rates (short reads) combined with
Low genetic variation
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Reads that do not require the expensive alignment step:
Notes: Let’s take a look at filtering opportunities based on the input reads.
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate (99.9%) and short (e.g., up to a few hundreds of DNA characters)
  Long reads: less accurate (85-90%) and long (e.g., from hundreds to millions of DNA characters)
Based on these, We leverage two filtering opportunities
First, we can filter exactly matching reads, which are reads that match exactly to one or more subsequences of the reference genome and do not require approximate string matching during alignment. Exact matches can frequently occur in short read sets with low sequencing errors and low genetic variations
Second, we can filter non-matching reads. Such reads do not have any potential matching locations in the reference genome can skip the expensive alignment step. Non-matching reads can frequently occur in long read sets with high sequencing errors and short or long read sets with high genetic variations

## Slide 18: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: by thorough analysis of mapping processes of reads with different properties and different degrees of genetic variation, we design two low-cost in-storage filters
[CLICK] 1) GenStore-EM for filtering exactly-matching reads
[CLICK] and 2) GenStore-NM for filtering most of the non-matching reads

## Slide 19: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: Let's take a closer look at GenStore-EM

## Slide 20: GenStore-EM
Efficient in-storage filter for reads with at least one exact match in the reference genome
Uses simple operations, without requiring alignment
Challenge: large number of random accesses per read to the reference genome and its index
Expensive random accesses to flash chips
Limited DRAM capacity inside the SSD
Notes: [CLICK] GenStore-EM accelerates read mapping by using an efficient in-storage filter to filter reads that have at least one exactly matching location in the reference genome
[CLICK] via simple operations, without requiring alignment.
The key challenge in designing GenStore-EM is the large number of random accesses to large data structures inside the SSD.
This is challenging because. [CLICK]
NAND flash memory exhibits poor performance for random access reads. [CLICK]
there is limited DRAM capacity available in SSD which is relatively small compared to the size of the data structures that need to be accessed.

## Slide 21: GenStore-EM: Data Structures
GCCCAAATGGTT
Read
GCC
CCC
…
K-mers
K-mer
Read-sized k-mers: to reduce the number of accesses per each read
Only one index lookup per read
Sorted read-sized k-mers: to avoid random accesses to the index
Sequential scan of the read set and the index
✓
✓
Notes: To reduce the **number** of accesses per each read, we introduce read-sized k-mers.
Therefore, instead of extracting several k-mers per read and performing index lookup for each of them, [CLICK] we can use the whole read as one k-mer
[CLICK] And have only one index lookup per read
[CLICK] To avoid **random** accesses to the index, we introduce the **sorted** index of read-sized k-mers.
[CLICK] This sorted index allows finding exact matches via sequential scanning of the read sets and the index

## Slide 22: GenStore-EM: Data Structures
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Sorted
Read-sized
K-mers
Read
AAAAAAAAAA
Notes: I show the key idea of GenStore-EM with a simplified example in which each short read consists of 10 characters.
Suppose that we have two data structures:
[CLICK] 1) a sorted read table, each entry of which stores a read [CLICK] and its unique ID, and
[CLICK] 2) a sorted k-mer index, which contains all unique read sized k-mers of the reference genome,
[CLICK] along with each k-mer’s corresponding locations in the reference genome.
[CLICK] Each data structure is sorted by read/k-mer in alphabetical order.

## Slide 23: GenStore-EM: Finding a Match
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read = K-mer
Next
Exact match  Filter the read
Next
Notes: We sequentially scan through these data structures in three different ways based on the [CLICK] comparison result of the current read and k-mer.
[CLICK] First, when the current read and k-mer are identical,
[CLICK] we record the read as an exactly-matching read that can be filtered from further read mapping process
[CLICK] Then, we move to the next element in both arrays. [CLICK]

## Slide 24: GenStore-EM: Not Finding a Match
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Next
Comparator
Read > K-mer
Notes: if the read is alphabetically larger than the k-mer,
we conclude that the k-mer does not match any read
and go to the next element in the index (so that we can examine if the next k-mer).

## Slide 25: GenStore-EM: Not Finding a Match
Next
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read < K-mer
Not an exact match  Send to read mapper
Notes: if the k-mer is alphabeticall larger than the read,
we conclude that the read does not match any k-mer in index, and needs to be sent for the full read mapping process
Then, we go to the next element in the sorted read table (so that we can examine the next read).
Using this technique, GenStore-EM avoids random accesses and performs filtering using only simple low-cost logic

## Slide 26: GenStore-EM: Not Finding a Match
Next
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted Read Table
ID | Read
873 | AAAAAAAAAA
232 | AAAAAAAAAG
17 | AAAAAAAACT
… | …
Sorted K-mer Index
Comparator
Read < K-mer
Not an exact match  Send to read mapper
Avoids random accesses
Simple low-cost logic
✓
✓
Notes: if the k-mer is alphabeticall larger than the read,
we conclude that the read does not match any k-mer in index, and needs to be sent for the full read mapping process
Then, we go to the next element in the sorted read table (so that we can examine the next read).
Using this technique, GenStore-EM avoids random accesses and performs filtering using only simple low-cost logic

## Slide 27: GenStore-EM: Optimization
Read-sized k-mer index takes up a large amount of space (126 GB for human index) due to the larger number of unique k-mers
K-mer | Loc.
AAAAAAAAAA | 1, 8, …
AAAAAAAAAC | 51
AAAAAAAAAT | 23, 37
… | …
Sorted K-mer Index
Strong Hash Value
1
4
7
16
Using strong hash values instead of read-sized k-mers
reduces the size of the index by 3.9x
Notes: Despite the key benefits of the sorted read-sized k-mer index, this index takes up a large space (126 GB for human index) due to the large number of unique read-sized k-mers.
We further reduce the overheads of GenStore-EM, by replacing read-sized k-mers with a strong hash of each read that act as
Sorting criterion
Fingerprint of each entry
Using strong hash values instead of read-sized k-mers reduces the size of the index by 3.9x
While this index is still larger than the baseline k-mer index used in the conventional read mappers, our proposal is feasible for in-storage processing due to the large capacity and high internal bandwidth of modern NAND flash-based SSDs.

## Slide 28: GenStore-EM: Design
GenStore-Enabled SSD
Host System
Die#1
Plane#1
Plane#2
Die#4
P#1
P#2
⋯
Die#1
P#1
P#2
Die#4
P#1
P#2
⋯
Die#1
P#1
P#2
Die#4
P#1
P#2
⋯
⋯
Channel#1
Channel#2
Channel#N
❷ Exact-match filtering
SSD Controller
NAND Flash Array
SRTable
SKIndex
❶ Sequential Reads
DRAM
Batch#i-1
Batch#i
Batch#j-1
Batch#j
Comparator
SRTable Buffer
SKIndex Buffer
Data is evenly distributed between channels, dies, and planes
to leverage the full internal bandwidth of the SSD
Steps 1 and 2 are pipelined.
During filtering, GenStore-EM sends the unfiltered reads
to the host system.
Notes: Now I show the overall operational flow of GenStore-EM, [CLICK]
with SRTable and SKIndex in the NAND flash memory, [CLICK]
distributed across all channels and dies. [CLICK]
And the comparator logic located on the SSD controller.
GenStore-EM consists of two steps: [CLICK]
Step 1 reads the two data structures from NAND flash chips to the SSD’s internal DRAM [CLICK] in a batched manner
Step 2 performs exact-match filtering within each read batch, using simple comparator logic.
Steps 1 and 2 are performed in a pipelined manner. During filtering, GenStore-EM sends the unfiltered reads to the host system for full read mapping.

## Slide 29: GenStore
GenStore-EM for Exactly-Matching Reads
GenStore-NM for Non-Matching Reads
Notes: Now, let’s take a closer look at GenStore-NM

## Slide 30: GenStore-NM
Efficient chaining-based in-storage filter to prune most of the non-matching reads
Challenge: how to perform chaining inside the SSD
  For a read with Seeds to , the chaining score for can be calculated as
i > j > 1
Costly dynamic programming on many seeds in each read
Particularly challenging for long reads with many seeds
Determine potential matching locations (seeds) in the reference genome
Prune some seeds in the reference genome
Determine the exact differences between the read and the reference genome
Seeding
Seed Filtering
(e.g., Chaining)
Alignment
Notes: Using chaing, GenStore-NM filters most of the nonmatching reads, i.e., reads that would not align to any subsequence in the reference genome. Recall that chaining filter calculates a similarity score for each read (called chaining score) and filters read with no high-scoring potential matching locations.
Calculating a chaining score in the SSD is challenging
because finding the best chaining score requires performing [CLICK] many iterations of a dynamic programming algorithm for all seeds within a read,
This is particularly challenging for long reads since they have a large number of k-mers per read

## Slide 31: GenStore-NM: Mechanism
  Filters many non-aligning reads without costly hardware resources in the SSD
Probability
Chart: 
Number of seeds per read
High Alignment Probability
Alignment
Reads with a sufficiently large number of seeds
are very likely to align to the reference genome
GenStore-NM uses a light-weight chaining filter
  Selectively performs chaining only on reads with a small number of seeds
  Directly sends reads that require more complex chaining to the host system
✓
Notes: [CLICK] To reduce the cost of chaining, GenStore-NM GenStore-NM uses a light-weight chaining filter
[CLICK] Selectively performs chaining only on reads with a small number of seeds
[CLICK] And Directly send reads that require more complex chaining to the host system
This idea is based on our observation from analyzing a wide range of real world genomic read sets.
[CLICK] This figure shows alignment probability of a read in a long read dataset to subsequences in the reference genome, as a function of the number of seeds per read.
[CLICK] We observe that reads with a sufficiently large number of seeds are very likely to align to subsequences in the reference
genome. Such reads can be directly sent to the CPU for full read mapping (bypassing the in-storage filter).
[CLICK] We conclude that the selective light-weight chaining approach can filter many non-aligning reads without costly hardware resources in the SSD

## Slide 32: GenStore-NM: Mechanism
  Can filter many non-aligning reads without costly hardware resources in the SSD
Probability
Chart: 
Number of seeds per read
High Alignment Probability
Alignment
Reads with a sufficiently large number of seeds
are very likely to align to the reference genome
GenStore-NM uses a light-weight chaining filter
  Selectively performs chaining only on reads with a small number of seeds
  Directly sends reads that require more complex chaining to the host system
Details on GenStore-NM’s design are in the paper
Notes: [CLICK] To reduce the cost of chaining, GenStore-NM GenStore-NM uses a light-weight chaining filter
[CLICK] Selectively performs chaining only on reads with a small number of seeds
[CLICK] And Directly send reads that require more complex chaining to the host system
This idea is based on our observation from analyzing a wide range of real world genomic read sets.
[CLICK] This figure shows alignment probability of a read in a long read dataset to subsequences in the reference genome, as a function of the number of seeds per read.
[CLICK] We observe that reads with a sufficiently large number of seeds are very likely to align to subsequences in the reference
genome. Such reads can be directly sent to the CPU for full read mapping (bypassing the in-storage filter).
[CLICK] We conclude that the selective light-weight chaining approach can filter many non-aligning reads without costly hardware resources in the SSD

## Slide 33: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: I will now go into our results

## Slide 34: Evaluation Methodology
Read Mappers
Base: state-of-the-art software or hardware read mappers
  Minimap2 [Bioinformatics’18]: software mapper for short and long reads
  GenCache [MICRO’19]: hardware mapper for short reads
  Darwin [ASPLOS’18]: hardware mapper for long reads
GS: Base integrated with GenStore
SSD Configurations
SSD-L: with SATA3 interface (0.5 GB/s sequential read bandwidth)
SSD-M: with PCIe Gen3 interface (3.5 GB/s sequential read bandwidth)
SSD-H: with PCIe Gen4 interface (7 GB/s sequential read bandwidth)
Notes: We valuate the following systems:
[CLICK] Base: state-of-the-art software or hardware read mappers for both short and long reads
[CLICK] GS: Base integrated with the GenStore inside the SSD
We evaluate these mappers on systems with various SSD configurations, a low-end, medium-end, and high-end SSD
For other details about our methodology, please refer to the paper.

## Slide 35: Performance – GenStore-EM
For a read set with 80% exactly-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Other | 170.17 | 69.24 | 154.65 | 74.71 | 159.07 | 73.31
Alignment | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 44 | 8.8 | 6.2857 | 2.8229 | 4.2832 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0
With the Software Mapper
With the Hardware Mapper
2.1× - 2.5× speedup compared to the software Base
1.5× – 3.3× speedup compared to the hardware Base
On average 3.92× energy reduction
29
2.5x
2.1x
2.1x
3.3x
1.5x
2.5x
Notes: We analyze the benefits of GenStore-EM for a 22-GB short read set where 80% of reads exactly match some subsequence in the reference genome and can be filtered.
We show the benefit of GS on software and hardware read mappers.
GS provides 2.1× - 2.5× speedup compared to the software Base
GS provides 1.5× – 3.3× speedup compared to the hardware Base
GS provides on average 3.92× energy reduction

## Slide 36: Performance – GenStore-NM
For a read set with 99.7% non-matching reads
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 1.564 | 5.362 | 0.78198 | 5.36 | 0.78198
Exec. time [sec]
Log scale
With the Software Mapper
With the Hardware Mapper
22.4× – 27.9× speedup compared to the software Base
6.8× – 19.2× speedup compared to the hardware Base
On average 27.2× energy reduction
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
22.4
29x
27.9x
19.2x
6.8x
6.8x
Notes: We analyze the benefits of GenStore-NM for a 12-GB long read set with very high genetic variation compared the the reference genome where 99.7% of reads do not match any subsequence in the reference genome.
We show the benefit of GS on software and hardware read mappers.
GS provides 22.4× – 27.9× speedup compared to the software Base
GS provides 6.8× – 19.2× speedup compared to the hardware Base
GS provides on average 27.2× energy reduction

## Slide 37: Area and Power
Based on Synthesis of GenStore accelerators using the Synopsys Design Compiler @ 65nm technology node
Logic unit | # of instances | Area [mm2] | Power [mW]
Comparator | 1 per SSD | 0.0007 | 0.14
K -mer Window | 2 per channel | 0.0018 | 0.27
Hash Accelerator | 2 per SSD | 0.008 | 1.8
Location Buffer | 1 per channel | 0.00725 | 0.37375
Chaining Buffer | 1 per channel | 0.008 | 0.95
Chaining PE | 1 per channel | 0.004 | 0.98
Control | 1 per SSD | 0.0002 | 0.11
Total for an 8-channel SSD | - | 0.2 | 26.6
Only 0.006% of a 14nm Intel Processor, less than 9.5% of the three ARM processors in a SATA SSD controller
Notes: We find area and power values of GenStore by synthesizing GenStore-EM and NM using 65nm technology node,
And find that for an 8-channel SSD, the area of GS is 0.2 mm square and the power is 26.6 watts
BY scaling the area to lower technology nodes, we observe that the area overhead of GS is 0.006% of an Intel processor and less than 9.5% of the of the three ARM processors in a SATA SSD controller.

## Slide 38: Other Results in the Paper
Effect of read set features on performance
  Data size (up to 440 GB)
  Filter ratio
Performance benefit of an implementation of GenStore outside the SSD
  In some cases, it provides performance benefits due more efficient streaming accesses
  Provides significantly lower benefit compared to GenStore
More detailed characterization of non-matching reads across different read mapping use cases and species
Notes: Let me briefly talk about other results that are included in the paper before concluding this talk. These include the following:

## Slide 39: Outline
Conclusions
Background
Motivation and Goal
Experimental Methodology
Temperature Analysis
Aggressor Row Active Time Analysis
Spatial Variation Analysis
Implications on Attacks and Defenses
Conclusions
Motivation and Goal
GenStore
Evaluation
Notes: Now, let me conclude by giving the summary.

## Slide 40: Conclusion
There has been significant effort into improving read mapping performance through efficient heuristics, hardware acceleration, accurate filters
Problem: while these approaches address the computation overhead, none of them alleviate the data movement overhead from storage
Goal: improve the performance of genome sequence analysis by effectively reducing unnecessary data movement from the storage system
Idea: filter reads that do not require the expensive alignment computation in the storage system to fundamentally reduce the data movement overhead
Challenges:
  Read mapping workloads can exhibit different behavior
  There are limited available hardware resources in the storage system
GenStore: the first in-storage processing system designed for genome sequence analysis to reduce both the computation and data movement overhead
Key Results: GenStore provides significant speedup (1.4x - 33.6x) and energy reduction (3.9x – 29.2x) at low cost
Notes: [CLICK] There has been significant effort into improving read mapping performance through efficient heuristics, hardware accelerators, and various filters that prune reads that do not require expensive computation.
[CLICK] While these approaches address the computation overhead in read mapping, None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated
[CLICK] Our goal is to Improve the performance of genome sequence analysis by effectively reducing unnecessary data movement from the storage system
[CLICK] The key idea is to Filter reads that do not require the expensive ASM computation in the storage system to fundamentally reduce the data movement overhead
CLICK] however, filtering reads inside SSD is challebging 1) Read mapping workloads can exhibit different behavior, and 2) There are limited available hardware resources in the storage system
[CLICK] To this end, we propose GenStore, The first in-storage processing system designed for genome sequence analysis to reduce both the computation/data movement overhead
[CLICK] GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines

## Slide 41: GenStore: A High-Performance In-Storage Processing System for Genome Sequence Analysis
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun,
Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr,
Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu
P&S SSD: Wednesday, 9 November 2022
Notes: Hi, I’m Nika, and today I will introduce GenStore: A High-Performance In-Storage Processing System
for Genome Sequence Analysis

## Slide 42: Backup Slides

## Slide 43: End-to-End Workflow of Genome Sequence Analysis
There are three key initial steps in a standard genome sequencing and analysis workflow
  Collection, preparation, and sequencing of a DNA sample in the laboratory
  Basecalling
  Read mapping
Genomic read sets can be obtained by
  Sequencing a DNA sample and storing the generated read set into the SSD of a sequencing machine
  Downloading read sets from publicly available repositories and storing them into an SSD
We focus on optimizing the performance of read mapping because sequencing and basecalling are performed only once per read set, whereas read mapping can be performed many times
  Analyzing the differences between a reads from an individual and many reference genomes of other individuals
  Repeating the read mapping step many times to improve the outcome of read mapping
Improving read mapping performance is critical in almost all genomic analyses that use sequencing
  45% of the execution time when discovering sequence variants in cancer genomics studies
  60% of the execution time when profiling the species composition of a multi-species (i.e., metagenomic) read

## Slide 44: Motivation
SSD-L
SSD-M
SSD-H
DRAM
Chart: 
| Base | SW-filtered | Ideal-ISF | Accelerator | Ideal-ISF+ACC
SSD-L | 97.56 | 76.6218 | 32.943 | 24.8 | 10.08
SSD-M | 78.44 | 55.588 | 25.1038 | 3.5428 | 1.44
SSD-H | 78.35 | 55.489 | 25.0669 | 2.0101 | 0.72203
DRAM | 75.16 | 51.98 | 1.6422
Chart: 
| Accelerator | ACC+Ideal-ISF
SSD-L | 24.8 | 10.08
SSD-M | 3.5428 | 1.44
SSD-H | 2.0101 | 0.72203
DRAM | 1.6422 | 1e-08
N/A
24.8
N/A
3.54
2.01
1.64
1.44
0.72
10.1
Execution time [sec]
ACC
SW-filter

## Slide 45: Motivation
State-of-the-art software read mapper, Minimap2
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
Base integrated with a software filter
that prunes 80% of exactly-matching reads
Base integrated with an
ideal in-storage filter
N/A
Notes: This plot shows the execution time of three read mapping systems.
Base refers to a State-of-the-art software read mapper, Minimap2
SW-filter refers to Base integrated with a software filter that prunes 80% of exactly-matching reads
Ideal-ISF refers to base integrated with an ideal in-storage filter than prunes 80% exactly matching reads inside the SSD

## Slide 46: Motivation
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
Low-end SSD with SATA3 interface (0.5 GB/s)
High-end SSD with PCIe Gen4 interface (7 GB/s)
Data preloaded in DRAM,
with no I/O overhead
N/A
Notes: To assess the impact of the storage subsystem, we evaluate each of the three mappers with different configurations
A low-end SSD, a high-end SSD, and DRAM which refers to an idealized scenario where all needed data is preloaded in DRAM with no I/O overhead

## Slide 47: Benefits of Ideal In-Storage Filter
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
The ideal in-storage filter significantly improves performance by
Reducing computation overhead
Reducing data movement overhead
N/A
Notes: Based on this plot, we make several observations, First…

## Slide 48: Overheads of Software Mappers
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
I/O has a significant impact on application performance
which can be alleviated at the cost of
expensive storage devices and interfaces
N/A
Notes: By comparing the high-end SSD, low-end SSD, and DRAM with no I/O overhead, we observe that
[CLICK] I/O has a significant impact on application performance
[CLICK] which can be alleviated at the cost of expensive storage devices and interfaces
However, it is challenging to scale a storage system’s capacity using only the high-end SSDs due to
[CLICK] the relatively smaller number of the PCIe slots in a server
[CLICK] And their significantly-higher prices

## Slide 49: Overheads of Software Mappers
Chart: 
| Base | SW-filter | Ideal-ISF
SSD-L | 97.56 | 76.6218 | 32.943
SSD-H | 78.35 | 55.489 | 25.0669
DRAM | 75.16 | 51.98
Execution time [sec]
SW-filter provides limited benefits compared to Base
N/A
The filtering process outside the SSD must compete
with the read mapping process for the resources in the system
Notes: Third, by comparing Base and SW-filter, we observe that despite a large number of needs that can be filtered, SW-filter does not provide significant benefits compared to base.
The limited speedup is mainly due to large number of accesses to the index structure for several k-mers per each read.
[CLICK] This shows that as opposed to the instorage filter, the filtering process outside the SSD must compete with the read mapping process for the resources in the system

## Slide 50: Overheads of Hardware Mappers
Chart: 
| Accelerator | Ideal-ISF
SSD-L | 24.8 | 10.08
SSD-H | 2.0101 | 0.72203
DRAM | 1.6422 | 1e-08
Execution time [sec]
24.8
10.1
23%
The ideal in-storage filter significantly improves performance
Even the high-end SSD does not fully alleviate the storage bottleneck
N/A
Notes: This figures shows similar analysis but with a state-of-the-art hardware read mapper, gencache, and its integration with the ideal in-storage filter.
We observe that Even the high-end SSD does not fully alleviate the storage bottleneck in this case
This is because by addressing computation overhead using the accelerator, I/O turns into a more serious bottleneck.
However, we observe that the ideal n-storage filter significantly improves performance since it addresses both the computation and data movement overheads.

## Slide 51: Ideal-OSF
Execution time of an ideal in-storage filter:
Execution time of an ideal outside-storage filter:
  60% slower than Ideal-ISF in our analysis

## Slide 52: Comparison to PIM
Even though read mapping applications could also benefit from other near-data, in-storage processing can fundamentally address the data movement problem by filtering large, low-reuse data where the data initially resides.
Even if an ideal accelerator achieved a zero execution time, there would still exist the need to bring the data from storage to the accelerator.
  2.15x slower than the execution time that Ideal-ISF+ACC provides in our motivational analysis
In-storage filter can be integrated with any read mapping accelerator, including PIM accelerators, to alleviate their data movement overhead.

## Slide 53: Long Read Use Cases

## Slide 54: FTL
GenStore-Enabled SSD
GenStore SSD Controller
Core
Core
Core
SSD-LV
ACC
DRAM
L2P
Mappings
Flash
Ctrl.#1
Flash
Ctrl.#N
⋯
⋯
CH-LV
ACC#1
CH-LV
ACC#N
GenStore
Metadata
① Start analysis
⑤ Unfiltered data
NAND
Die#4
NAND
Die#1
⋯
NAND
Die#4
NAND
Die#1
⋯
③ Full-bandwidth read
② Preparation
Flush
Load
GenStore
FTL
④ Filtering
Host System
❷
❸
❶

## Slide 55: FTL: Metadata
GenStore metadata includes the mapping information of the data structures necessary for read mapping acceleration
In accelerator mode, GenStore also keeps in internal DRAM other metadata structures of the regular FTL
  Examples include the page status table and block read counts which need to be updated during the filtering process
We carefully design GenStore to only sequentially access the underlying NAND flash chips while operating as an accelerator
  Requires only a small amount of metadata to access the stored data

## Slide 56: FTL: Data Placement
GenStore needs to properly place its data structures to enable the full utilization of the internal SSD bandwidth
When each data structure is initially written to the SSD, GenStore sequentially and evenly distributes it across NAND flash chips
GenStore can specify the physical location of a 30-GB data structure by maintaining only the list of 1,250 (30 GB/24 MB) physical block addresses
It significantly reduces the size of the necessary mapping information from 300 MB (with conventional 4-KiB page mapping) to only 5 KB (1,250 4 bytes)

## Slide 57: FTL: SSD Management Tasks
In accelerator mode, GenStore only reads data structures to perform filtering, and does not write any new data
  GenStore does not require any write-related SSD-management tasks such as garbage collection and wear-leveling
The other tasks necessary for ensuring data reliability can be done before or after the filtering process
  GenStore significantly limits the amount of data whose retention age would exceed the manufacturer-specified threshold since GenStore’s filtering process takes a short time.
  GenStore-FTL can easily avoid read disturbance errors for data with high read counts since GenStore sequentially reads NAND flash blocks only once during filtering

## Slide 58: Data Sizes
Conventional k-mer index in Minimap2 + reference genome: 7 GB (k = 15)
Read-sized k-mer index before optimization: 126 GB (k= 150)
Read-sized k-mer index after optimization: 32 GB (k = 150)

## Slide 59: SSD Specs
SSD-L: SATA3 interface (0.5 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  8 channels
SSD-L: PCIe Gen3 M.2 interface (3.5 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  16 channels
SSD-L: PCIe Gen4 interface (7 GB/s sequential read)
  1.2 GB/s per channel bandwidth
  16 channels

## Slide 60: Evaluation Methodology
Performance modeling
  Ramulator for DRAM timing
  MQSim for SSD timing
  We model the end-to-end throughput of GenStore based on the throughput of each GenStore pipeline stage
    Accessing NAND flash chips
    Accessing internal DRAM
    Accelerator computation
    Transferring unfiltered data to the host
Real system results
  AMD EPYC 7742 CPU
  1TB DDR4 DRAM
  AMD μProf
Notes: I won’t go into details, but you can refer to our paper for more details about our evaluation methdology.

## Slide 61: GenStore-NM
GenStore-Enabled SSD
Host System
Flash Array
Input
Read Set
SSD Controller
DRAM
KmerIndex
Seed Finder
Location Buffer
① Reads
Chaining-Based Filter
(Filters low-score reads)
❸
M ≤ # of Seeds < N
Seed Count-Based Filter
(Filters if # of Seeds < M)
❷
# of Seeds ≥ N
High chaining score
❶
④ Seeds
③ Query
K-mer Window
Hash Acc.
K-mers
②

## Slide 62: Chaining Processing Element

## Slide 63: GenStore-EM
Chart: 
| Base | SIMD | GS-Ext | GS | Base | SIMD | GS-Ext | GS | Base | SIMD | GS-Ext | GS | SSD-L | SSD-M | SSD-H
Other | 101.8 | 128.44 | 119.24 | 52.78 | 73.98 | 81.378 | 31.69 | 31.69 | 86.17 | 94.787 | 31.92 | 31.92
Alignment | 68.37 | 16.46 | 16.46 | 16.46 | 80.67 | 43.02 | 43.02 | 43.02 | 72.9 | 41.39 | 41.39 | 41.39
Chart: 
| Base | GS-Ext | GS | Base | GS-Ext | GS | Base | GS-Ext | GS | SSD-L | SSD-M | SSD-H
 | 44 | 108.4 | 8.8 | 6.2857 | 15.4857 | 2.8229 | 4.2832 | 7.7429 | 2.8229
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Exec. time [sec]
44
108
15
GS-Ext provides significant performance improvements
over both Base and SIMD in SSD-M and SSD-H.
GS-Ext provides limited benefits over SIMD in SSD-L
due to low external I/O bandwidth.
Notes: GS-Ext provides significant performance
improvements over both Base and SIMD in SSD-M and SSD-H. However,
GS-Ext provides limited benefits over SIMD in SSD-L since
its performance is bottlenecked by the low external I/O bandwidth.

## Slide 64: GenStore-NM
Chart: 
| Base | GS | Base | GS | Base | GS | SSD-L | SSD-M | SSD-H
Time | 34.84 | 1.5537 | 22.55 | 0.77687 | 21.72 | 0.77687
Chart: 
| Base | GS-Ext | GS | Base | GS-Ext | GS | Base | GS-Ext | GS | SSD-L | SSD-M | SSD-H
 | 30.028 | 30.056 | 1.564 | 5.362 | 4.2937 | 0.78198 | 5.36 | 2.1469 | 0.78198
GS-Ext performs significantly slower than Base (2.28x - 1.91x)
on all systems.
Notes: GS-Ext performs significantly slower than Base (2.28x - 1.91x) on all systems.

## Slide 65: Effect of Inputs on GenStore-EM
Normalized exec. time
Read set size:
Exact match:
Chart: 
| 75% | 85% | 75% | 85% | 75% | 85% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.50504 | 0.30763 | 0.27598 | 0.19436 | 0.28937 | 0.16534
Chart: 
| 75% | 85% | 75% | 85% | 75% | 85% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.65906 | 0.65906 | 0.33838 | 0.33838 | 0.31986 | 0.31986

## Slide 66: Effect of Inputs on GenStore-NM
Chart: 
| 0.3% | 37% | 0.3% | 37% | 0.3% | 37% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.029734 | 0.68811 | 0.03427 | 0.67399 | 0.035084 | 0.66259
Chart: 
| 0.3% | 37% | 0.3% | 37% | 0.3% | 37% | 1x | 10x | 20x
Base | 1 | 1 | 1 | 1 | 1 | 1
GS | 0.14589 | 0.37024 | 0.14582 | 0.37002 | 0.14581 | 0.37001
Normalized exec. time
Read set size:
Align. rate:
0.69
0.67
0.66